## Slide 1
4
Seat Belt Requirements – FMVSS No. 208
Vehicle Type * | Gross Vehicle Weight Rating | Seat Belt Requirement **
All Buses | <= 10,000 lbs. | Lap/shoulder belts for all DSPs
Medium over-the-road (Motorcoach) | 10,000 - 26,000 lbs. | Lap/shoulder belts for all DSPs
Medium other buses | 10,000 - 26,000 lbs. | Belt for driver only
Large school bus | > 10,000 lbs. | Belt for driver only
Transit bus | > 26,000 lbs. | Belt for driver only
Large Other Buses, including motorcoaches | > 26,000 lbs. | Lap/shoulder belts for all DSPs
* All have more than 10 Designated Seating Positions ** Some exclusions may apply |  | 
Definitions

## Slide 2
Other Occupant Protection Standards for Buses
School Buses
            FMVSS No. 220, School bus rollover protection
                FMVSS No. 221, School bus body joint strength
                FMVSS No. 222, School bus passenger seating and crash protection
                FMVSSs No. 131, School bus pedestrian safety devices
                FMVSS Nos. 108 and 111 – Signal lamps for conspicuity and mirrors for driver 3600 visibility
                FMVSS No. 301, 303, 304, and 305 – fuel system integrity
Buses with GVWR <10,000 lbs.
FMVSS No. 216, Roof crush resistance
FMVSS No. 226, Ejection mitigation
Other crash avoidance and crashworthiness standards applicable to light vehicles
Motorcoaches and Other Large Buses
FMVSS No. 136, Electronic stability control (ESC) systems for heavy vehicles
All Buses
FMVSS No. 217, Bus emergency exits and window release and retention
Safety standards for lighting, mirrors, controls, displays, tires, brakes, doors, locks, seats, material flammability, etc.