## Slide 1: Proposal for an achievable, cost effective Security Concept for EOBRs
C. Hardinge / A. Lindinger

## Slide 2: Content
Problem domain
Solution
  General
  PKI
  Digital Signature
  Data Storage
  Certification
  Roadside Enforcement
Summary

## Slide 3: Problem Domain
RODS Data is stored at different system nodes with no inherent protection
Data can be modified without leaving any trace
Enforcement cannot rely on the data
Basic security goals not achieved:
  data integrity
  authenticity
  non-repudiation
EOBR
Host System servers
Enforcement servers
Secure communication
Secure communication
Possible point of manipulation
Enforcement device
Secure communication

## Slide 4: Solution – General
Focus on the protection of the data, not the communication path
  Protecting the complete communication path is costly and does not solve the problem of maintenance of data integrity
  Protecting the data allows cost effective transmission and storage of the data
  Any modification of the data, intentional or accidental can be easily detected
  Roadside enforcement can rely on the data authenticity, non-repudiation and integrity
  The data is protected using digital signatures provided by a Public Key Infrastructure (PKI) implementation
    State of the art. Encouraged by NIST for federal agencies (800-25)

## Slide 5: Solution – Public Key infrastructure

## Slide 6: Solution – Public Key infrastructure
Bob‘s Private
Key BOB_SK
Bob‘s Public
Key BOB_PK
RA
Registration
Authority
Is Bob Bob ?
Is Bob trustworthy?
Certification
Authority
CA‘s Private
Key CA_SK
Please
trust me
OK to create certificate
Bob’s Public Key
Certificate data
Signature CA_SK
Generate certificate and sign with CA_SK

## Slide 7: Solution – Digital Signature with asymmetrical cryptography
Hash Function
Message
Signature
EOBR
Private Key
Encryption
Digest
Message
Decryption
Expected
Digest
Actual
Digest
Hash Function
Signer - EOBR
Receiver - Enforcement
Channel
Digest
Algorithm
Digest
Algorithm
EOBR certificate
Validated EOBR Public Key
EOBR certificate

## Slide 8: Solution – Data Storage
Data storage based on RODS flat file format. New elements needed.
Data Element | Data Element Definition | Type | Length | Sign
EOBR ID | Unique ID of the EOBR – same ID as in the certificate. | N | 10 - TBD | Yes
Session Begin | Date and time of session begin | N | 15 | Yes
Session End | Date and time of session end | N | 15 | Yes
Digital Signature | ASCII representation of Digital Signature of all relevant data elements since the last Digital Signature was recorded | A | 40-500 | No
Certificate | ASCII representation of an EOBR public key certificate | A | 130-1050 | No
Record Signed | Indicates whether the record has been signed or not (optional depending on data storage concept – see 4.1.3.3) | A | 1 | 

## Slide 9: Solution – Data Storage
Digital signatures calculated only using relevant original data
Maximum flexibility provided, to maintain existing storage concepts
Example of a simplified RODS file structure showing a Session with digital signature:
Could interleave annotations but would need a „sign“ element.

## Slide 10: Solution – Data Storage Rules
At least the following rules must be applied (non exhaustive list):
  whenever a new Session is started, a Session Begin is recorded
  whenever a Session is finished a Session End is recorded
  each Session must include an EOBR ID record
  the Digital Signature is calculated for all records between, and including, the Session begin and end records
  the Digital Signature is stored in the RODS file directly after the Session End
  the EOBR Certificate is stored in the RODS file directly after the Digital Signature
  the element Event Update Status Code must be excluded from the signature calculation (Sign = N)
  the EOBR must ensure that only, and all original records are signed, not annotations, regardless of the source of the annotation
  annotated records must not replace original records.

## Slide 11: Solution – Certification
Independent EOBR certification is needed to ensure that the critical security and functional elements of the system are handled correctly and consistently by all manufacturers:
  EOBR generation, storage and processing of HOS/RODS records
  key generation and installation
  key storage
  Interoperability of EOBRs and enforcement devices
The detailed EOBR security requirements must be defined in order to be able to perform a certification
Possible certification standard: Common Criteria
An EOBR and its manufacturer must have achieved security certification before they are permitted to install any “hot” keys.

## Slide 12: Solution – Roadside Enforcement
Roadside enforcement is the central issue of the EOBR. Without efficient enforcement, the EOBR is superfluous.
With digitally signed data, roadside enforcement can rely on:
  the integrity of the data
  the authenticity of the data
  non-repudiation not being feasible
An analysis of HOS using signed data and all data could be compared to determine the effect of the annotations

## Slide 13: Solution – Roadside Enforcement scenarios
Full Telematic solution
EOBR
Host System servers
Enforcement servers
Secure comms
Secure comms
Enforcement Device
Secure comms
Secure comms
EOBR
Host System servers
Enforcement Device
Secure P2P comms
EOBR
Enforcement Device
Secure P2P communication
P2P / Telematic mixed solution
Full Peer to Peer solution

## Slide 14: Solution – Roadside Enforcement Equipment
It is recommended that the enforcement community be equipped with standard, dedicated mobile enforcement devices
Such a device could support:
  USB interface
  Short range wireless interface
  Long-range wireless interface (if needed)
  Secure record storage until return to back-office
  Software upgrade in back-office
  Accepted interface to enforcement system
This would be a robust, standardized and long term cost effective solution.

## Slide 15: Summary
Implementing the proposed PKI based security concept for data protection provides the following advantages:
  Deliberate or accidental modification of data is detectable
  Trustable data for enforcement – no more „comic books“
  Simple, flexible, cost effective solution
  Reduced opportunities for driver harassment
  Supports following FMCSA requirements:
    Data at rest must be protected
    Data in Transit must be protected
    The EOBR shall protect EOBR data collected, stored, disseminated, or transmitted from inadvertent alteration, spoofing, tampering, and other deliberate corruption

## Slide 16: Questions
  Any questions ?
  Charles Hardinge
    +49 7721 67-2365
    Charles.Hardinge@continental-corporation.com
  Andreas Lindinger
    +49 7721 67-2245
    Andreas.Lindinger@continental-corporation.com